- Requerimientos Técnicos - Descripción de Embarcaciones de Apoyo

El alcance del trabajo será el establecido en el Anexo II – Alcance del Servicio.

Sujeto a lo estipulado en el mencionado Anexo, se solicitarán las cantidades de embarcaciones que define el Anexo II según las siguientes características:

- PSV 240,  DP2

- FSIV / FSV, DP2 Gross Tonnage < (less than) 500 Tn.

Notas:

- Las embarcaciones estarán operando durante todo el proyecto como Soporte a las Operaciones de la Plataforma Autoelevable, en el Área 02

- Los puertos de operaciones para las actividades de apoyo  logístico serán los puertos de API Dos Bocas Tabasco y, dependiendo de la opción que se aplique según lo establecido en el Anexo II, API Coatzacoalcos, Veracruz.

A continuación, se listan las características principales de las Embarcaciones de Apoyo requeridas para dar soporte logístico a las actividades de la Plataforma Autoelevable:

PSV 240   DP- 2 Specifications

Year Built: Less than 10 years of service.

Characteristics:

Length Overall:         			         240 ft.

Capacities

Drill Water 			min 500 m3

Potable Water 			min 180 m3

Fuel	   			500/600 m3

Liquid Mud 			Min 600 m3

Dry Bulk 				Min. 200 m3

Cargo Deck

Tonnage 				Min 1,400 MT

Clear Area 			               650/700 m2

Electronics & Controls

DP 2

AIS System

Satellite Internet

Satellite Phone

Accommodation

Fully Air-conditioned

Special Equipment

FIFI  1- 2 System

Life Rafts

Rescue Boat (SOLAS)

Capability to install and operate a ROV.

Certifications/Vetting

CLASS Company Certification (no pending issues)

IMCA Inspection performed during the last 6 months before February 15th 2019

National Maritime Authority of Mexico (Certifications and Regulations)

Certification for Transport Dangerous Residues and Residues of special handling (SERMARNAT)

FSIV  / FSV   DP2 Specifications

Year Built: Less than 10 years of service.

Characteristics:

Length overall 			170/200 ft

Gross Tonnage 			< (less than) 500 MT

Transit Speed: 			18/ 20 Knots

Capacities

Cargo Deck Area 			Min 250m3

Cargo Deck Loading 		Min 400 MT

Fuel Capacity			Min (120/130m3)

Liquid Mud 			Min 150m3

Rig Water Capacity 		102m3

Potable Water Capacity 		Min 10/15 m3

Accommodation

Fully Air-conditioned

Accommodations for 10 people

Certified to carry min 40 Passengers as Crew Boat

Electronics & Controls

DP 2

AIS System

Satellite Internet

Satellite Phone

Special Equipment

FIF1-2 System

Life Rafts

Rescue Boat (SOLAS).

Certifications/ Vetting

CLASS Company Certification (no pending issues)

IMCA Inspection performed during the last 6 months before February 15th, 2019.

National Maritime Authority of Mexico (Certifications / Regulations)

Certification for Transport Dangerous Residues and Residues of special handling (SERMARNAT)

- Embarcaciones de Relevo /Adicional.

El oferente deberá prever el uso de una embarcación Relevo / Adicional tipo PSV (DP2) (200” – 240”) la cual será inspeccionada y aprobada por la Empresa.

Será “Relevo” de las embarcaciones de apoyo ante eventuales contingencias durante el período que dure la misma.

Será “Adicional” cuando por necesidades logísticas, la operación requiera otro barco de manera temporal, para complementar la actividad. (Transporte cajas de recorte, fluidos, etc.)

- Seguros

DOF: 23/06/2016

DISPOSICIONES Administrativas de carácter general que establecen las reglas para el requerimiento mínimo de seguros a los Regulados que lleven a cabo obras o actividades de exploración y extracción de hidrocarburos, tratamiento y refinación de petróleo y procesamiento de gas natural.

4   Especificaciones técnicas de las Embarcaciones propuestas

El oferente deberá completar la información correspondiente a las Embarcaciones de Apoyo ofertadas de acuerdo a lo especificado en la tabla al final de este Anexo.

Se deberá completar una planilla por Embarcación de Apoyo y una por la Embarcación Relevo / Adicional.

En caso que alguna característica no corresponda al tipo de embarcación, por favor indicarlo en el casillero correspondiente.

| General | Vessel Offered |
| --- | --- |
| Vessel Name (Current/Previous) - Specify all names |  |
| IMO number / Official number |  |
| Flag |  |
| Classification (If changed in last 12 months name of previous classification society and date of change) |  |
| Class Notation - Specify Full Notation |  |
| Place and Year of Build - Specify Yard and Year |  |
| Type of Vessel |  |
| Call Sign |  |
| Vessel’s Satcom, email, fax and telex numbers |  |
| Ice Class (specify) |  |
| Deck Strength (if applicable) |  |
| Helipad |  |
| Ownership and Operation |  |
| Registered owner (full style, address and contact details) |  |
| Technical manager (full style , address and contact details) |  |
| Commercial Manager (full style, address and contact details) |  |
| Disponent Owners (if applicable) (full style, address and contact details) |  |
| Dry-docking and Surveys |
| Date of last dry-dock |  |
| Date next dry-dock due (see 13.2) |  |
| Date of last annual survey |  |
| Date of last special survey( |  |
| Dimensions |
| L.O.A (m) |  |
| Breadth (m) |  |
| Depth Moulded (m) |  |
| Draft (Max) (m) |  |
| Draft Design (m) |  |
| Deadweight/Tonnage |
| Deadweight (DWT) |  |
| Gross Registered Tonnage (GRT) |  |
| Net Registered Tonnage |  |
| Propulsion |
| Main Engines + Auxiliary Engines. Specify number and type |  |
| Main Propulsion Power (BHP) |  |
| Power output (kW) |  |
| Emergency Power - Specify type |  |
| Propellers - Specify number and Fixed or CP. |  |
| Bow Thruster - Specify number and power |  |
| Stern Thruster - Specify number and power |  |
| Azimuth Thruster - Specify number and power |  |
| Rudders - Specify number |  |
| Bollard Pull (AHTS) |
| Continuous (t) |  |
| Achievable (t) |  |
| At Full Electrical Load (t) |  |
| Manoeuvring Equipment |
| Dynamic Positioning System - Specify IMO Equip. Class |  |
| Main engines |  |
| Joystick |  |
| Speed & Fuel Consumption (Tons/Day) |
| In port - Specify speed and fuel consumption |  |
| Cruising Speed - Specify speed and fuel consumption |  |
| Full Speed - Specify speed and fuel consumption |  |
| In DP/Station keeping Mode |  |
| Bunker SECTION 4 - SPECIFICATIONS AND TECHNICAL DOCUMENTSs |
| Bunker SECTION 4 - SPECIFICATIONS AND TECHNICAL DOCUMENTSs |  |
| Deck Equipment |
| Crane (t) - Specify number and rating |  |
| Crane Outreach (m) - Specify max |  |
| Windlass - Specify number and rating |  |
| Capstans (aft) - Specify number and rating |  |
| Tugger winch - Specify number and rating |  |

| Tank Capacities |
| --- |
| Total Fuel Oil (m3) |  |
| Max. Fuel Oil Cargo (m3) - Specify amount for delivery |  |
| Drill Water (m3) |  |
| Potable Water (m3) |  |
| Brine (m3) |  |
| Base Oil (m3) |  |
| Liquid Mud (m3) |  |
| Bulk (m3) |  |
| Oil Dispersant (m3) |  |
| Oil Recovery (m3) |  |
| Ballast (m3) |  |
| Special Tanks (m3) |  |
| Discharge Rates |
| Fuel Oil (m3/hr) |  |
| Drill Water (m3/hr) |  |
| Potable Water (m3/hr) |  |
| Liquid mud (m3/hr) (also state if pumps are Centrifugal or Positive Displacement and if drive is hydraulic or electric) |  |
| Bulk (m3/hr) |  |
| Brine (m3/hr) |  |
| Baseoil (m3/hr) |  |
| Deck Load |
| Max Deck Load (t) |  |
| Deck Area (m2) |  |
| Deck Strength (tons/m2) |  |
| Reefer Connections - Specify number and power supply |  |
| Anchor Handling & Towing Equipment |
| Winches |  |
| Type |  |
| Capacity |  |
| Brake Load |  |
| Line Pull |  |
| Emergency Release System |  |
| Rope Reel Winch |  |
| Stern Roller |  |
| Shark Jaws |  |
| Karm Forks |  |
| Towing Pins |  |
| Chain Locker Capacities |  |
| A-Frame |  |
| Deck Crane |  |
| Dry brake coupling |  |
| Work wires |  |
| Tow wires |  |
| Spare Wires |  |
| Bridge Equipment |
| Radars |  |
| Gyros |  |
| GPS |  |
| DGPS |  |
| Speed Log |  |
| Echo Sounder |  |
| Auto-Pilot |  |
| Wind/Speed Direct |  |
| Magnetic Compass |  |
| Communication Equipment |
| GMDSS |  |
| Radio |  |
| Inmarsat |  |
| Navtex |  |
| VHF Radio |  |
| VHF Portable |  |
| UHF Portable |  |
| EPIRB |  |
| SARTS |  |

| Accommodation |
| --- |
| Crew |  |
| Passenger |  |
| Public Rooms/Rescue |  |
| Fire Fighting |
| FiFi System |  |
| CO2 Fixed System |  |
| Life Saving Equipment |
| Life rafts |  |
| Fast Rescue Craft |  |
| Daughter Craft (ERRV) |  |
| Immersion Suits |  |
| Smoke Hoods |  |
| Jason’s Cradle |  |
| H2S Masks |  |
| Additional Ratings |
| Green Class/Green Passport |  |
| Oil Recovery Capability |  |
| Insurance |
| Employers Liability, Workmen’s Compensation and Occupational Disease Insurance, including an Alternative Employer endorsement (where applicable) (US $) - Specify amount per occurrence |  |
| Comprehensive General Liability Insurance (US $) - Specify amount per occurrence |  |
| Comprehensive Liability Automobile/Motor Insurance (US $) - Specify amount per occurrence |  |
| Hull and Machinery Insurance including war risk. Name, style and address / contact details of H&M insurers Insured value: |  |
| Name, style, address and contact details of War risks insurers: |  |
| Protection and Indemnity Insurance including wreck and debris removal and pollution liability Name, style, address and contact details of P&I insurers Amount of pollution liability cover |  |
| Crew Information |
| [Specify minimum manning level required during operations: all the roles /ranks required and the number of each role / rank required] | Rank Number |
| Please specify any other requirements in relation to manning for example |  |
| Experience of Master and Officers; Time served in rank Time served on vessel Time served on Specific Vessel Type Area of operations Number of Rig moves (AHTS) Towing experience (AHTS) (For any operations within the 500m zone of any installation, it should be noted that Unmanned Machinery Spaces (UMS) procedures should not be used and there should be 2 Mariners on the bridge). |  |
| Nationality of officers: Nationality of crew: |  |
| Winch operator – detail name, time in role, experience, when and where trained |  |
| DP officers: detail number required, experience / qualifications required of each: Last activities as DP operators. If officers and / or crew supplied by Manning Agency give name and full style, address and contact details of Agency |  |
| Provide details and demonstrate that vessel complement is qualified, vessel suitably manned for 24 hour operations and compliant with STCW 2010 Manila hours of rest requirements. |  |
| Crew change schedule |  |
| Confirm common language used on vessel |  |

Electronic Copies of the following items must be provided;

Ship Certificates (as applicable)

Certificate of Class

International Tonnage Certificate

International Load Line Certificate

International Oil Pollution Prevention Certificate

International Ship Security Certificate

DGMM Certificate

Safety Management Certificate

SOLAS Safety Equipment Certificate and Supplement

SOLAS Safety Construction Certificate

Safety Radio Certificate

Certificate of Financial Responsibility (COFR)

Certified Bollard Pull

Civil Liability for Bunker Oil Pollution Damage certificate (CLBC)

Civil Liability Convention Certificate (CLC) (if applicable)

| Documents/Drawings |
| --- |
| Vessel Spec Sheet |  |
| Class Status Report |  |
| DP System FMEA (Latest Version) 2 | 1. Should be submitted along with description of action list closeout Response. 2. As a minimum, the vessel FMEA must meet IMCA standards 3. FMEA clearly defines safest mode of operation, the worse case failure(s) and significant 4. Single point failures in the summary. 5. FMEA has been updated after any major modifications and proving trials have been conducted. 6. FMEAs are required to have vessel specific: Details of governor failure modes Details of AVR failure modes Details of main switchboard control power failure modes Details of position reference system processing provided by the DP control system Details of DP control system consequence analysis feature DP control system Input/Output Schedule Details of Networks Satellite based position references one line diagram Hydro-acoustic position references one line diagram Other position reference systems (e.g. Taut Wire, Laser based etc) one line diagram(s) Details of communications and alert systems provided for the DP operator and their redundancy (systems and power supply) |
| FMEA Proving Trials |  |
| Annual DP Trial Results3 |  |
| Date of last DP trials |  |
| DP Anniversary date (see clause 9.15.6) |  |
| DP Capability Plots4 | To include conditions for: Intact condition at 1.0kts, 1.5kts, and 2.0kts current Displaying vessel effects of worst case failure at 1.0kts, 1.5kts, and 2.0kts current Displaying vessel effects of most common failure |
| Lifting Equipment/Winches Inspections | Crane Curves Wire Certificates Latest Inspections Load Tests |
| Tank Plan | Provide a plan indicating dedicated tanks, Capacity and max SG for each tank |
| IMCA - CMID (Common Marine Inspection Document)1. OVID- OCIMF (Oil Companies International Marine Forum) | IMCA prefered |
| GA Plan (including back deck layout and winch configuration) |  |
| Vessel Operating Manual |  |
| DP Operating Manual |  |
| ROV Operations Capabilities | Description of Installation and Operation places. |